## Slide 1: FPGA Systems & Digital Electronics
IHL Kick-Off Meeting, Siegen
17. July 2026
Dr.-Ing. Michael Karagounis Professor of Electronics University of Applied Sciences and Arts Dortmund

## Slide 2: FPGA Education & Research Activities
Training & Education
Research & Development
ASIC Test Platform
Data Acquisition System
Detector & Slow Control
Low-Latency Trigger System
AI/ML Acceleration
Real-Time Data Processing / Online Event Reconstruction
SEE Verification & Emulation
Digital Design Fundamentals
HDLs Verilog/VHDL
Verification
Synthesis & Implementation
Debugging (ILA)
SoC Design (Zynq)
Embedded (Peta)Linux
High-Speed Links
Notes: Die Spannungswandler, die wir im Rahmen des Forschungsprojektes entwickeln, kommen für Experimente im Bereich der Hochenergiephysik am Large Hadron Collider, also dem Teilchenbeschleuniger am Cern, zum Einsatz. Der Teilchenbeschleuniger befindet sich in etwa 100m unterhalb der Erdoberfläche an der Grenze zwischen der Schweiz und Frankreich und besitzt eine Gesamtlänge von etwa 27km. In einem solchen Teilchenbeschleuniger werden Teilchen auf sehr hohe Energien beschleunigt und zur Kollision gebracht. Hiervon erhofft man sich experimentelle Erkenntnisse im Bereich der Teilchenphysik zu erlangen. Ein großer Erfolg, war z.B. der experimentelle Nachweis des Higgs Boson.
Der Kollisionspunkt dieser Teilchen wird von einem Detektor umschlossen, wie z.B. im ATLAS Experiment der ALTAS Detektor.
Das Herzstück bildet der sogenannte Pixeldetektor, der sich im inneren der gesamten Detektoranalge befindet. Hier werden die Partikel, die bei der Teilchenkollision entstanden sind mit Hilfe von Pixelsensoren detektiert und über weitere Elektronik ausgewertet. Die Sensoren und die Elektronik des Chips befinden sich auf Pixelmodulen welche fassförmig innerhalb des Pixeldetektors angeordnet sind.

## Slide 3: Synergy with ChipsEDU of DE:SIGN Initiative
Open Educational Resources to strengthen Germany‘s chip design work-force
Low-cost hardware platform based on the Gatemate FPGA of Cologne Chip AG
Open-Source Software development software based on OneWare Studio
Teaching Material
  Basic & advanced design course
  Lecture scripts
  Video Lectures
  Step-by-Step Tutorials
  Hands-On lab exercises

## Slide 4: Exemplary FPGA Based Testsystem for Radiation Characterization of RISC-V microcontrollers

## Slide 5: Digital IC Design Education & Research Activities
Training & Education
Research & Development
Pixel Detector Readout
Digital-Assisted Analog Circuits / Mixed-Signal Circuits
On-Detector Intelligence
  Embedded RISC- V
  AI/ML Accelerators
  In Memory Computing
Embedded FPGA Integration
  post-production flexibility
LPDDR interfaces
Heterogenous integration 2.5 interposers & chiplet
Basic understanding of digital CMOS circuits on transistor level
Tooling Tutorials
  Constraining
  Synthesis
  Floorplanning
  Macro Integration
  Implementation
  Power/Timing
  Signoff Verification
Verification
  UVM/Cocotb
Radiation Tolerant Design
  TMR
  ECC
  Scrubbing
Notes: Die Spannungswandler, die wir im Rahmen des Forschungsprojektes entwickeln, kommen für Experimente im Bereich der Hochenergiephysik am Large Hadron Collider, also dem Teilchenbeschleuniger am Cern, zum Einsatz. Der Teilchenbeschleuniger befindet sich in etwa 100m unterhalb der Erdoberfläche an der Grenze zwischen der Schweiz und Frankreich und besitzt eine Gesamtlänge von etwa 27km. In einem solchen Teilchenbeschleuniger werden Teilchen auf sehr hohe Energien beschleunigt und zur Kollision gebracht. Hiervon erhofft man sich experimentelle Erkenntnisse im Bereich der Teilchenphysik zu erlangen. Ein großer Erfolg, war z.B. der experimentelle Nachweis des Higgs Boson.
Der Kollisionspunkt dieser Teilchen wird von einem Detektor umschlossen, wie z.B. im ATLAS Experiment der ALTAS Detektor.
Das Herzstück bildet der sogenannte Pixeldetektor, der sich im inneren der gesamten Detektoranalge befindet. Hier werden die Partikel, die bei der Teilchenkollision entstanden sind mit Hilfe von Pixelsensoren detektiert und über weitere Elektronik ausgewertet. Die Sensoren und die Elektronik des Chips befinden sich auf Pixelmodulen welche fassförmig innerhalb des Pixeldetektors angeordnet sind.

## Slide 6: Relaxation Oscillator Design
S
R
Q
QB
Vc1
Vc2
With CAN, data is transmitted without a clock signal
CAN nodes require their own oscillator for synchronization
MOPS uses a relaxation oscillator
Two capacitors are alternately charged and discharged
S
R

## Slide 7: Compensation for Production Variations
To ensure stable CAN communication, the oscillator frequency must not vary by more than 3%.
frequency trimming introduced
configurable capacitance value
Oscillator frequency is influenced by
process variations
temperature
radiation

## Slide 8: Automatic Frequency Calibration
The bit timing functionality of the CAN protocol unit performs phase correction by default to establish synchronization between the transmitter and receiver
Phase error signal of the bit timing unit is fed to a digital PI controller, which trims the frequency of the oscillator.
PI Compensator
part of CAN protocol unit

## Slide 9: STRV Microcontroller Architecture
AIRES RISC-V core from Fraunhofer IMS
  RV32-IMC Core
  3 stage pipeline
JTAG Interface
  JTAG TAP & debug module
  Non-volatile debug ROM with debug ISR
Peripherals
  Memory mapped registers
  UART
  GPIOs
32KByte Dual Port SRAM
Separate power domains for
  RISC-V Core
  SRAM
  periphery und pad ring
thing-gate-oxide core-transistor-only implementation for high TID robustness

## Slide 10: SEE Protection Scheme of Logic
Full Triple modular redundancy (TMR)
  Triplication of combinatoric logic & FFs
  Three clock trees
  Three majority voter
  15 µm distance between triplicated instances
STRV-1 has even three pads for clock, reset and JTAG
SEU counter counts corrected SEUs per domain
  SEU detection signals of all majority voters OR-ed
  detects one SEU per clock cycle per domain

## Slide 11: SEE Protection Scheme of SRAM
Scrubbing with ECC
  Data is stored in SRAM protected by ECC (e.g., Hamming code)
  Memory is read cyclically
  Detected errors are corrected
  Corrected data is written back
Problem
  Hardening level of address logic in commercial SRAM macros is unknown
  If the address decoder is hit, corrected data may be written to the wrong address
Scrubbing with Triplication
  3 SRAM macros are written/read in parallel
  Allows for multiple bit error correction
  Has huge chip area penalty

## Slide 12: STRV-1/2 Microcontroller Features
2 mm
2 mm
1.5 mm
1.5 mm
STRV-1 (65nm)
STRV-2 (28nm)
 | STRV-1 | STRV-2
Frequency | 50 MHz | 100 MHz
Supply Voltage | 1.2V | 0.9V
Power with Scrubbing | 20 mW | 17 mW
Power without Scrubbing | 15 mW | 12 mW
TID hardness | 1 Gigarad | 1 Gigarad
SEE hardness | 2.2 SEFI/h @ 109 p/cm²/s | -

## Slide 13: TID Characterization with X-Rays
STRV-1 (65nm)
STRV-2 (28nm)

## Slide 14: Preliminars SEE Heavy Ion Characterization Results of 28nm Design STRV-2
No crashes observed
  No call of the trap handler, UART data arrive timely and free of errors
Resets seldomly observed
  Execution time of benchmark reduced signifcantly
  SEU registers reset to zero
SEU in Power-On-Control circuit triggers low-active reset
Variation of benchmark execution time

## Slide 15: SEE Injection Simulation Framework
Testbench based on VPI functions
Post-synthesis/implementation netlist processed
physical position of cells included from DEF file
SEU/SET/Marco fault injection
PRNG for randomness and reproduceability
Filtering options: nodes/cell-names/cell-type
Modified SRAM and standard cell libraries to avoid x at timing violations
Automatic generation of assertions to check correct implementation of TMR

## Slide 16: Dataflow Optimized Flexible AI/ML Accelerator
Goals:
  high data throughput at low power consumption
  Flexibility by parameterization & run-time configurability
Solution:
  Identification of the overall systems bottleneck e.g. memory or sensor bandwidth
  Adaption of the accelerator to the system constraints
Process element matrix scalable in X and Y direction to define parallelism
Scalable L1 /L2 memories sizes to influence locality of data processing and meet bandwidth requirements
Programmability of the processing sequence during runtime e.g. spatial/temporal distribution
Data coding that restricts flexibility is avoided e.g. bitmaps instead of RLC, CSS in the feature maps

## Slide 17: Map Space Exploration & Compilation
automatic optimized mapping of neural networks to custom hardware
high degree of flexibility leads to a high number of possible for a use case
determination of performance characteristics at hardware level is time-consuming
optimization based on an abstract model preferable
compiler translates configurations into intermediate representations
  MLIR Framework (Multilevel Intermediate Representation)
Evaluation using cascaded cost models e.g. for memory accesses, peak bandwidth, runtime, pre- / post-processing,
Cascading allows fast evaluation of configurations
Optimal configuration is reduced to executable binary representation

## Slide 18: Extracted performance metrics
inference accuracy for ImageNet (classification 1000 classes)
  AlexNet: top 5 accuracy, 80.1% (float32: 79.5%)
  MobileNetV2: top 5 accuracy, 89.4% (float32: 92.7%)
  post training 8 bit quantization
hardware performance in 28 nm TSMC:
  area requirement IP core: < 0.5 mm²
  power consumption: ~ 10 mW / 4.4 TOPS/W
Throughput:
  AlexNet: ~ 10 FPS, MobileNet ~ 30 FPS
Dataset: ImageNet / ILSVRC2012 :
  1000 classes, 250x250 px
  No. of images: 1.3 million
Model: MobileNet v2
  50 layers
  weights and feature maps 1 kB - 1 MB per layer with 8-bit quantization

## Slide 19: Demo – MobileNet v2
Neural Network | Mobilenet v2
Input Resolution | 224 x 224 px
Layers | 52 x convolution, 1 x linear
Parameters | 3.5 million
Operations | 300 MOP
Performance | max. 12.5 FPS, 3.8 GOP/s (int8)

## Slide 20: Custom Demo – „ScrewNet“
Neural Network | Custom
Input Resolution | 512 x 640 px
Layers | 36 x convolution
Parameters | 363000
Operations | 2.85 GOP
Performance | max. 1.5 FPS, 4.3 GOP/s (int8)

## Slide 21: Take-Home Message
Intelligent detector electronics require expertise across the complete digital design chain
Training & Education
  FPGA & ASIC design methodologies
  Modern EDA workflows
  Hands-on hardware platforms
Research & Development
  Radiation-hard digital systems
  Embedded computing
  AI-enabled detector electronics
  Reconfigurable ASIC technologies
The Intelligent Hardware Lab
  A shared platform enabling next-generation digital electronics for future particle physics experiments.