## Slide 1: All-Si Project in Göttingen
Nana Chychkalo
Jörn Grosse-Knetter
Arnulf Quadt

## Slide 2: All-Si in Göttingen
In cooperation with Bonn : All-Si – an all-silicon ladder of CMOS detectors
Concept of All-Si ladder:
  Single piece of silicon
  Several sensors cut from the wafer
  Post-processing of wafer
Project within DRD3
Göttingen’s contribution funded by BMBF
Starting with thermo-mechanical simulation in Göttingen

## Slide 3: All-Si Ladder
Design towards an All-Si ladder:
  Several CMOS chips cut out of wafer with handling area to sides
  RDL connecting from cable at side of ladder to CMOS chips
  Cooling: is air flow sufficient?

## Slide 4: All-Si Simulation
Need thermo-mechanical simulations to assess cooling needs
Getting familiar with simulation packages (Ansys, CAD programs) → licenses available, already in use
Assume properties as expected for next LF Monopix prototype:
  Chip size 22 mm x 30 mm, thinned to 0.04 mm (except for edges and end-pieces) → Vchip = 2.6·10 -8 m3
  Power consumption per chip: 1.5 W
    Assumed to be homogeneous
    To be sub-divided in pixel area and periphery later
    To add later: power from voltage drop on RDL
  Total power density: 5.68·107 W/m3

## Slide 5: All-Si Simulation: Steady State
First step: steady-state thermal simulation
Checks heat distribution, assuming convection of 300 W/m3 °C

## Slide 6: All-Si Simulation: Transient
Transient thermal analysis: evolution of temperature vs time
Variation implemented: convection changes from 300 to 50 W/m3 °C

## Slide 7: All-Si Simulation: Air Flow
Move from convection to air flow cooling:
  Integrate the fluent software module in Ansys (operated separately from mechanical simulation)
  Check amount of flow required to keep CMOS chips below a reasonably low temperature

## Slide 8: Summary
Pursuing design and later production of an All-Si ladder of CMOS detectors with Bonn
Started thermo-mechanical simulations:
  Simulation based on basic chip power consumption specs → to be refined
  Steady-state and transient mechanical simulation in operation
  Air flow work beginning now
Aim: estimate air flow cooling needs for All-Si ladder